FERRARI CALIFORNIA TECHNICAL SPECIFICATIONS

DIMENSIONS AND WEIGHTS

Length 4563 mm

Width 1902 mm

Height 1308 mm

Wheelbase 2670 mm

Front track 1630 mm

Rear track 1605 mm

Dry weight 1630 kg

Kerb weight 1735 kg

Weight distribution 47% Front - 53% Rear

Fuel tank capacity 78 l

Boot capacity 340 l

240 (with roof retracted)

TYRES

Front 245/40 ZR19"

Rear 285/40 ZR19"

Front (optional) 245/35 ZR20"

Rear (optional) 285/35 ZR20""

CARBON-CERAMIC BRAKES

Front 390 x 34 mm

Rear 360 x 32 mm

ELECTRONIC CONTROL SYSTEMS

CST with F1-TRAC Stability and Traction Control System

TPTMS Tyre Pressure and Temperature

Monitoring System

ENGINE

90° V8 Direct Injection

Bore and stroke 94 x 77.37 cc

Overall displacement 4297 cc

Compression ratio 12.2:1

Maximum power output 338 kW (460 CV) at 7750 rpm

Maximum torque 485 Nm (49 kgm) at 5000 rpm

PERFORMANCE

Maximum speed 310 km/h

0-100 km/h under 4.0 sec

0-400 m 12.2 sec

0-1.000 m 22.1 sec

GEARBOX

F1, dual-clutch, 7-speed plus reverse

Manual 6-speed + REV

SUSPENSION

Front: Double wishbone

Rear: Multilink

FUEL CONSUMPTION

ECE Combined* 13.1 l/100 km

CO2 EMISSIONS

ECE Combined* 305.6 g/km

*Europe version